## Slide 1
DIGITAL MODULATION TECHNIQUES WITH REAL-WORLD APPLICATIONS
Presented by:Om Shinde
Anuj Shinde
Dhananjay Sharma
Pratik Shinde

## Slide 2
Contents
  Introduction
  Amplitude Shift Keying (ASK)
  Frequency Shift Keying (FSK)
  Phase Shift Keying (PSK)
  Comparison and Conclusion

## Slide 3
  Digital modulation is the process of converting digital data (binary bits 0 and 1) into an analog waveform by varying one or more characteristics of a carrier signal — such as its amplitude, frequency, or phase — to enable transmission over communication channels.
  It allows efficient, noise-resistant wireless communication.
  Common digital modulation techniques include:
ASK (Amplitude Shift Keying)
FSK (Frequency Shift Keying)
PSK (Phase Shift Keying)
Introduction

## Slide 4
  In ASK, the amplitude of the carrier wave changes according to digital data.
  A binary ‘1’ turns the carrier ON, and ‘0’ turns it OFF.
  It is simple and cost-effective but sensitive to noise.
Real-World Example:
RFID Tags use ASK to transmit stored ID data to RFID readers through electromagnetic coupling.
Formula: s(t)=Amcos⁡(2πfct)
Amplitude Shift Keying (ASK)

## Slide 5
  FSK changes the frequency of the carrier depending on whether the input bit is 0 or 1.
  Two discrete frequencies represent logic levels:
At Bit 1 the frequency of output wave increases
At Bit 0 the frequency of output wave decreases
  It offers better noise immunity than ASK.
Real-World Example:
  Bluetooth uses Gaussian FSK (GFSK) to enable low-power, short-range wireless communication between devices.
Frequency Shift Keying (FSK)

## Slide 6
  Phase Shift Keying (PSK) is a digital modulation technique in which the phase of a constant-amplitude carrier is changed whenever the input bit changes. In Binary PSK (BPSK):
  Bit ‘0’ → Phase = 0°
  Bit ‘1’ → Phase = 180°
  Each bit transition causes a 180° phase shift, allowing reliable representation of digital data.
Real-World Example:
Wi-Fi uses PSK and higher-order variants (like QPSK, 16-QAM) for high-speed data transmission.
Formula:
s(t)=Acos⁡(2πfct+ϕi)
Phase Shift Keying (PSK)

## Slide 7
Comparison and Conclusion
  Digital modulation enables efficient, reliable wireless data communication.
  ASK → RFID, FSK → Bluetooth, PSK → Wi-Fi demonstrate how modulation is chosen based on application needs for range, power, and speed.
  Python simulations help visualize signal behavior and improve understanding of digital communication systems.

## Slide 8
References
  S. Haykin, Communication Systems, 5th Edition, Wiley, 2013.
  K. Finkenzeller, RFID Handbook: Fundamentals and Applications, 3rd Edition, Wiley, 2010.
  Bluetooth SIG, Bluetooth Core Specification v5.4, 2021.
  IEEE Std 802.11-2020, IEEE Standard for Wi-Fi Networks, 2020.
  MATLAB & Simulink, Digital Modulation Techniques Tutorial, MathWorks. [Online]. Available: https://www.mathworks.com/help/comm/ug/digital-modulation.html